3D gravity inversion by planting anomalous densities
Leonardo Uieda and Valéria C. F. Barbosa
Observatório Nacional
August, 2011

---
Outline

---
Outline
Forward Problem

---
Outline
Forward Problem
Inverse Problem

---
Outline
Forward Problem
Inverse Problem
Planting Algorithm
Inspired by René (1986)

---
Outline
Forward Problem
Inverse Problem
Planting Algorithm
Inspired by René (1986)
Synthetic Data

---
Outline
Forward Problem
Inverse Problem
Planting Algorithm
Inspired by René (1986)
Synthetic Data
Real Data

---
Forward problem

---
Surface of the Earth

---
Surface of the Earth
Observations
      of
g_z

---
Surface of the Earth
Observations
      of
g_z
Group in a vector:
{color blue bold g} = left [ {color blue stack{g_1 # g_2 # dotsvert # g_N} } right ]_{N times 1}
color blue bold g
 = observed data

---
color blue bold g
 = observed data

---
color blue bold g
 = observed data
Assume caused by
anomalous sources

---
color blue bold g
 = observed data
Assume caused by
anomalous sources
Density contrast =
%DELTA %rho

---
Parametrize the gravitational effect

---
Parametrize the gravitational effect
Linearize

---
Parametrize the gravitational effect
Linearize
Interpretative model
Discretize into
M elements

---
Parametrize the gravitational effect
Linearize
Interpretative model
jth element
Right rectangular prisms
Homogeneous density contrast
color green p_j
 (Nagy et al., 2000)
Discretize into
M elements

---
Parametrize the gravitational effect
Linearize
Interpretative model
Arrange M density contrasts in a vector:
{color green bold p} = left [ {color green stack{p_1 # p_2 # dotsvert # p_M} } right ]_{M times 1}
Parameter vector
Discretize into
M elements

---
Parametrize the gravitational effect
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
Predicted data
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
Predicted data
Gravitational effect is linear
{color red bold d} = sum from j=1 to M {{color green p_j}{bold a}_j}
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
Predicted data
Gravitational effect is linear
{color red bold d} = sum from j=1 to M {{color green p_j}{bold a}_j}
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Density contrast of jth prism
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
Predicted data
Gravitational effect is linear
{color red bold d} = sum from j=1 to M {{color green p_j}{bold a}_j}
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Effect of prism with unit density
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
Predicted data
Gravitational effect is linear
{color red bold d} = sum from j=1 to M {{color green p_j}{bold a}_j} = bold A color green bold p
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
Predicted data
Gravitational effect is linear
{color red bold d} = sum from j=1 to M {{color green p_j}{bold a}_j} = bold A color green bold p
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Parameter vector
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
Predicted data
Gravitational effect is linear
{color red bold d} = sum from j=1 to M {{color green p_j}{bold a}_j} = bold A color green bold p
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Jacobian (sensitivity) matrix
Discretize into
M elements

---
Parametrize the gravitational effect
{color blue bold g} approx {color red bold d}
Predicted data
Gravitational effect is linear
{color red bold d} = sum from j=1 to M {{color green p_j}{bold a}_j} = bold A color green bold p
color green p_j = %DELTA %rho
Prisms with
not shown
color green p_j = 0
Column vector of A
Discretize into
M elements

---
Solved forward problem:
{color red bold d} = sum from j=1 to M {{color green p_j}{bold a}_j}
color red bold d
color green bold p

---
How to do the inverse?
?
color green bold hat p
color blue bold g

---
Inverse problem

---
Minimize difference between

---
Observed data
color blue bold g
Minimize difference between

---
Predicted data
color red bold d
color blue bold g
Minimize difference between
and

---
color red bold d
color blue bold g
Minimize difference between
and
bold r = color blue bold g - color red bold d

---
color red bold d
color blue bold g
Minimize difference between
and
bold r = color blue bold g - color red bold d
Residual vector

---
color red bold d
color blue bold g
Minimize difference between
and
bold r = color blue bold g - color red bold d
Residual vector
%phi(color green bold p) = ldline bold r rdline_2 = left ( sum from i=1 to N ({color blue g}_i - {color red d}_i )^2 right )^{1 over 2}
Data-misfit function:

---
color red bold d
color blue bold g
Minimize difference between
and
bold r = color blue bold g - color red bold d
Residual vector
%phi(color green bold p) = ldline bold r rdline_2 = left ( sum from i=1 to N ({color blue g}_i - {color red d}_i )^2 right )^{1 over 2}
Data-misfit function:
 ℓ2-norm of r
Least-squares fit

---
ill-posed problem
non-existent
non-unique
non-stable

---
constraints
ill-posed problem
non-existent
non-unique
non-stable

---
constraints
ill-posed problem
well-posed problem
non-existent
exist
non-unique
unique
non-stable
stable

---
Constraints:
1. Compact

---
Constraints:
1. Compact
no holes inside

---
Constraints:
1. Compact
no holes inside
2. Concentrated around “seeds”

---
Constraints:
Similar to René (1986)
1. Compact
no holes inside
2. Concentrated around “seeds”

---
Constraints:
Similar to René (1986)
1. Compact
no holes inside
2. Concentrated around “seeds”
User-specified prisms

---
Constraints:
Similar to René (1986)
1. Compact
no holes inside
2. Concentrated around “seeds”
User-specified prisms
Given density contrasts
%rho_s

---
Constraints:
Similar to René (1986)
1. Compact
no holes inside
2. Concentrated around “seeds”
User-specified prisms
Given density contrasts
%rho_s
Any n° of ≠ density contrasts
Not like René (1986)

---
Constraints:
Similar to René (1986)
1. Compact
no holes inside
2. Concentrated around “seeds”
User-specified prisms
Given density contrasts
%rho_s
Any n° of ≠ density contrasts
3. Only
or
color green p_j = 0
color green p_j = %rho_s
Not like René (1986)

---
Constraints:
Similar to René (1986)
1. Compact
no holes inside
2. Concentrated around “seeds”
User-specified prisms
Given density contrasts
%rho_s
Any n° of ≠ density contrasts
3. Only
or
color green p_j = 0
color green p_j = %rho_s
Not like René (1986)
4.
of closest seed
color green p_j = %rho_s

---
constraints
ill-posed problem
well-posed problem
Minimize data misfit
Minimize goal function
%phi(color green bold p) = ldline bold r rdline_2 = left ( sum from i=1 to N ({color blue g}_i - {color red d}_i )^2 right )^{1 over 2}
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)

---
constraints
ill-posed problem
well-posed problem
Minimize data misfit
Minimize goal function
%phi(color green bold p) = ldline bold r rdline_2 = left ( sum from i=1 to N ({color blue g}_i - {color red d}_i )^2 right )^{1 over 2}
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
Regularizing parameter

---
constraints
ill-posed problem
well-posed problem
Minimize data misfit
Minimize goal function
%phi(color green bold p) = ldline bold r rdline_2 = left ( sum from i=1 to N ({color blue g}_i - {color red d}_i )^2 right )^{1 over 2}
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
Regularizing function

---
constraints
ill-posed problem
well-posed problem
Minimize data misfit
Minimize goal function
%phi(color green bold p) = ldline bold r rdline_2 = left ( sum from i=1 to N ({color blue g}_i - {color red d}_i )^2 right )^{1 over 2}
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
%mu
= tradeoff between fit and regularization
Regularizing function

---
Regularization:
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
%theta(color green bold p) = sum from j=1 to M { {color green p_j}over{{color green p_j} + %epsilon} l_j^{`%beta}}

---
Regularization:
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
Similar to
Silva Dias et al. (2009)
%theta(color green bold p) = sum from j=1 to M { {color green p_j}over{{color green p_j} + %epsilon} l_j^{`%beta}}

---
Regularization:
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
Similar to
Silva Dias et al. (2009)
%theta(color green bold p) = sum from j=1 to M { {color green p_j}over{{color green p_j} + %epsilon} l_j^{`%beta}}
%epsilon
= avoid singularity
l_j
= distance between jth prism and seed
%beta
= how much compactness
(3 to 7)

---
Regularization:
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
%theta(color green bold p) = sum from j=1 to M { {color green p_j}over{{color green p_j} + %epsilon} l_j^{`%beta}}
For
color green p_j <> 0
:

---
Regularization:
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
%theta(color green bold p) = sum from j=1 to M { {color green p_j}over{{color green p_j} + %epsilon} l_j^{`%beta}}
For
color green p_j <> 0
:
distance from seeds

---
Regularization:
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
%theta(color green bold p) = sum from j=1 to M { {color green p_j}over{{color green p_j} + %epsilon} l_j^{`%beta}}
For
color green p_j <> 0
:
distance from seeds
regularizing function

---
Regularization:
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
%theta(color green bold p) = sum from j=1 to M { {color green p_j}over{{color green p_j} + %epsilon} l_j^{`%beta}}
For
color green p_j <> 0
:
distance from seeds
regularizing function
Imposes:
Compactness
Concentration around seeds

---
Constraints:
1. Compact
Regularization
2. Concentrated around “seeds”
3. Only
or
color green p_j = 0
color green p_j = %DELTA %rho_s
4.
of closest seed
color green p_j = %DELTA %rho_s

---
Constraints:
1. Compact
Regularization
2. Concentrated around “seeds”
3. Only
or
color green p_j = 0
color green p_j = %DELTA %rho_s
Algorithm
4.
of closest seed
color green p_j = %DELTA %rho_s

---
Planting Algorithm

---
Overview:
Based on René (1986)

---
Overview:
Based on René (1986)
Start with seeds

---
Overview:
Based on René (1986)
Start with seeds

---
Overview:
Based on René (1986)
Start with seeds
known density contrast & position

---
Overview:
Based on René (1986)
Start with seeds
known density contrast & position
All other parameters set to 0

---
Overview:
Based on René (1986)
Start with seeds
known density contrast & position
All other parameters set to 0
Iteratively grow

---
Overview:
Based on René (1986)
Start with seeds
known density contrast & position
All other parameters set to 0
Iteratively grow
add neighbor of seed

---
Overview:
Based on René (1986)
Start with seeds
known density contrast & position
All other parameters set to 0
Iteratively grow
add neighbor of seed
accretion

---
Overview:
Based on René (1986)
Start with seeds
known density contrast & position
All other parameters set to 0
Iteratively grow
add neighbor of seed
accretion
Controlled by goal function and data misfit function
%phi(color green bold p) = ldline bold r rdline_2 = left ( sum from i=1 to N ({color blue g}_i - {color red d}_i )^2 right )^{1 over 2}
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)

---
Algorithm:

---
Algorithm:
Define interpretative model
Interpretative model

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
Interpretative model

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
Interpretative model

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
Interpretative model

---
Algorithm:
Define interpretative model
All parameters zero
seeds
N_S
Include seeds
Seeds
Prisms with
not shown
color green p_j = 0

---
Algorithm:
Define interpretative model
All parameters zero
seeds
N_S
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - {color red bold d}^{(0)}
Prisms with
not shown
color green p_j = 0

---
Algorithm:
Define interpretative model
All parameters zero
seeds
N_S
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - {color red bold d}^{(0)}
Residual vector
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - {color red bold d}^{(0)}
Observed data
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
color red bold d
= predicted data
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - {color red bold d}^{(0)}
Predicted by seeds
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
color red bold d
= predicted data
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - {color red bold d}^{(0)}
color red bold d = sum from j=0 to M color green p_j {bold a}_j
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
color red bold d
= predicted data
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - {color red bold d}^{(0)}
Many
`=0
color red bold d = sum from j=0 to M color green p_j {bold a}_j
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
color red bold d
= predicted data
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - {color red bold d}^{(0)}
color red bold d = sum from s=1 to N_S color green %rho_s {bold a}_{j_S}
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
color red bold d
= predicted data
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
color red bold d
= predicted data
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
Density contrast
of sth seed
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
color red bold d
= predicted data
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
Column vector
of A
Prisms with
not shown
color green p_j = 0

---
Algorithm:
color blue bold g
= observed data
Define interpretative model
All parameters zero
seeds
N_S
color red bold d
= predicted data
Include seeds
Compute initial residuals
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
Neighbors
Find neighbors of seeds
Prisms with
not shown
color green p_j = 0

---
Growth:
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
j = chosen
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
color green p_{j} = %rho_s
(New elements)
j = chosen
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
new predicted data
color green p_{j} = %rho_s
(New elements)
j = chosen
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
new predicted data
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = color blue bold g - {color red bold d}^{(new)}
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
new predicted data
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = color blue bold g - {color red bold d}^{(new)}
j
{color red bold d}^{(old)} +` effect `of `j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
new predicted data
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = color blue bold g - {color red bold d}^{(new)}
j
{color red bold d}^{(old)} +` effect `of `j
sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}}
{color green p_j} {bold a}_j
`+ `
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
new predicted data
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = color blue bold g - {color red bold d}^{(new)}
j
{color red bold d}^{(old)} +` effect `of `j
sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}}
{color green p_j} {bold a}_j
`+ `
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
new predicted data
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = color blue bold g - sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} - {color green p_j} {bold a}_j
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
new predicted data
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = color blue bold g - sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} - {color green p_j} {bold a}_j
j
{bold r}^{(0)}
Prisms with
not shown
color green p_j = 0
{

---
Growth:
Try accretion to sth seed:
%phi(color green bold p) = ldline bold r rdline_2
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
%GAMMA(color green bold p) = %phi(color green bold p) + %mu %theta(color green bold p)
new predicted data
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
Variable sizes
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
j
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
(New elements)
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
j
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
j
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
At least one seed grow?
Yes
No
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
At least one seed grow?
Yes
No
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
At least one seed grow?
Yes
No
j
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0
j

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
j
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0

---
Growth:
Try accretion to sth seed:
Choose neighbor:
1. Reduce data misfit
2. Smallest goal function
N_S
color green p_{j} = %rho_s
j = chosen
Update residuals
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
None found = no accretion
At least one seed grow?
Yes
No
Prisms with
not shown
color green p_j = 0
Done!

---
Advantages:
Compact & non-smooth
Any number of sources
Any number of different density contrasts
No large equation system
Search limited to neighbors

---
Remember equations:
Initial residual
Update residual vector
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}

---
Remember equations:
Initial residual
Update residual vector
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
No matrix multiplication (only vector +)

---
Remember equations:
Initial residual
Update residual vector
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
No matrix multiplication (only vector +)
Only need some columns of A

---
Remember equations:
Initial residual
Update residual vector
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
No matrix multiplication (only vector +)
Only need some columns of A
Calculate only when needed

---
Remember equations:
Initial residual
Update residual vector
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
No matrix multiplication (only vector +)
Only need some columns of A
Calculate only when needed
& delete after update

---
Remember equations:
Initial residual
Update residual vector
{bold r}^{(0)} = color blue bold g - left( sum from s=1 to N_S {color green %rho_s {bold a}_{j_S}} right)
{bold r}^{(new)} = {bold r}^{(old)} - {color green p_j} {bold a}_{j}
No matrix multiplication (only vector +)
Only need some columns of A
Calculate only when needed
& delete after update
Lazy evaluation

---
Advantages:
Compact & non-smooth
Any number of sources
Any number of different density contrasts
No large equation system
Search limited to neighbors

---
Advantages:
Compact & non-smooth
Any number of sources
Any number of different density contrasts
No large equation system
Search limited to neighbors
No matrix multiplication (only vector +)
Lazy evaluation of Jacobian

---
Advantages:
Compact & non-smooth
Any number of sources
Any number of different density contrasts
No large equation system
Search limited to neighbors
No matrix multiplication (only vector +)
Lazy evaluation of Jacobian
Fast inversion + low memory usage

---
Synthetic Data

---
Sources = 1 km X 1 km X 1 km

---
%DELTA %rho = 0.5` g/cm^3
Sources = 1 km X 1 km X 1 km

---
%DELTA %rho = 0.5` g/cm^3
%DELTA %rho = 1.0` g/cm^3
Sources = 1 km X 1 km X 1 km

---
Depth = 0.8 ` km
Sources = 1 km X 1 km X 1 km

---
Depth = 0.8 ` km
Depth = 1.6 ` km
Sources = 1 km X 1 km X 1 km

---
Depth = 0.8 ` km
Depth = 1.6 ` km
Sources = 1 km X 1 km X 1 km
Data set = 375 observations

---
Depth = 0.8 ` km
Depth = 1.6 ` km
Sources = 1 km X 1 km X 1 km
Data set = 375 observations
Area = 5 km X 3 km

---
Depth = 0.8 ` km
Depth = 1.6 ` km
Sources = 1 km X 1 km X 1 km
Data set = 375 observations
Area = 5 km X 3 km
0.05 mGal Gaussian noise

---
Interpretative model = 151,875 prisms
Prisms = 66.7 m X 66.7 m X 66.7 m

---
Used 2 seeds

---
Placed in center of sources
Used 2 seeds

---
Placed in center of sources
Used 2 seeds
With corresponding density contrasts

---
%DELTA %rho = 0.5` g/cm^3
Placed in center of sources
Used 2 seeds
With corresponding density contrasts

---
%DELTA %rho = 0.5` g/cm^3
%DELTA %rho = 1.0` g/cm^3
Placed in center of sources
Used 2 seeds
With corresponding density contrasts

---
Inversion result

---
Inversion result

---
compact
concentrated around seeds
Inversion result
recover correct geometry of sources

---
Predicted data
compact
concentrated around seeds
Inversion result
recover correct geometry of sources

---
Observed data
Predicted data
compact
concentrated around seeds
Inversion result
recover correct geometry of sources

---
Observed data
Predicted data
compact
concentrated around seeds
Inversion result
recover correct geometry of sources
fits observations

---
Observed data
Predicted data
375 data
On laptop with 2.0 GHz
151,875 prisms
Total time
` approx 4.4 ` min

---
Real Data

---
After Carminatti et al. (2003)

---
Cana Brava complex (CBC)
After Carminatti et al. (2003)

---
Cana Brava complex (CBC) & Palmeirópolis sequence (PVSS)
After Carminatti et al. (2003)

---
Cana Brava complex (CBC) & Palmeirópolis sequence (PVSS)
Outcropping
North of Goiás
Tocantins Province
Amazonian & São Francisco cratons
After Carminatti et al. (2003)

---
Cana Brava complex (CBC) & Palmeirópolis sequence (PVSS)
Gravimetric data:
132 observations
Residual Bouguer
Max 45 mGal
After Carminatti et al. (2003)

---
Cana Brava complex (CBC) & Palmeirópolis sequence (PVSS)
Previous interpretation:
Carminatti et al. (2003)
%DELTA %rho = 0.27 g/cm^3
PVSS
%DELTA %rho = 0.39 g/cm^3
CVC
Max depth
`approx 6 km
After Carminatti et al. (2003)

---
Cana Brava complex (CBC) & Palmeirópolis sequence (PVSS)
Previous interpretation:
Carminatti et al. (2003)
%DELTA %rho = 0.27 g/cm^3
PVSS
%DELTA %rho = 0.39 g/cm^3
CVC
Max depth
`approx 6 km
Test this hypothesis
After Carminatti et al. (2003)

---
Assign seeds
Assign seeds
Green:
z = 0 km
%DELTA%rho = 0.27 g/cm^3
Blue:
z = 2 km
%DELTA%rho = 0.27 g/cm^3
Red:
z = 0 km
%DELTA%rho = 0.39 g/cm^3
Total = 269

---
Interpretative model
Size: 120 km X 50 km X 11 km
Prism size: 500 m X 500 m X 575 m
480,000 prisms

---
Inversion result

---
Inversion result

---
Inversion result
Observed data
Predicted data

---
Inversion result

---
Inversion result

---
Inversion result

---
Inversion result

---
Inversion result

---
Inversion result

---
Inversion result
Max depth
Compact
`approx 6 km
Agree with previous interpretation
Fits observations

---
Inversion result
132 data
On laptop with 2.0 GHz
480,00 prisms
Total time
` approx 3.75 ` min

---
Conclusions

---
Conclusions
- New 3D gravity inversion
- Multiple sources
- Interfering gravitational effects
- Abrupt density-contrast distribution
- No matrix multiplication
- No need to solve large linear systems
- Ideal for: ore bodies, intrusions, salt domes, etc

---
Previous and future work
Developed for gravity gradients
Presented at EAGE 2011 preliminary results
To be presented at SEG 2011:
Final results
Robust method to handle non-targeted sources

---
Thank you